Directions: Circle or completely mark through the letter of the one most correct alternative.

1.	For hand-threading operations, round split dies are held in a tool called a:

a.	Die stock. 			b.  Die handle.

c.	Die holder. 			d.  Die key.

2.	The distance from a point on a screw thread to a corresponding point on the adjacent thread is called the:

a.	Pitch. 			b.  Lead.

c.	Axial length. 		d.  Helical distance.

e.	None of the above.

3.	The distance a screw thread advances along its axis in one   revolution is called the:

a.	Pitch. 			b.  Lead.

c.	Axial length. 		d.  Helical distance.

e.	None of the above.

4.	The smallest diameter of a screw thread is called the:

a.	Pitch Diameter. 		b.  Basic diameter.

c.	Major diameter.		d.  Minor diameter.

e.	None of the above.

5.	Which of the following designations describes an internal screw thread that has a close precision fit:

a.	¾-10 UNC 1A LH. 		b.  5/16-24 UNF 2A.	 	c.  7/16-20 UNF 2B.

d.	½-16 UNS 3B. 		e.  10-32 UNF 1B. 		f.  ¼-20 UNC 3A.

6.	The thread form most used for producing traversing movements on machine tools, such as the lead screw on a lathe, is the

a.	Whitworth. 			b.  Square.

c.	Acme. 			d.  Worm.

7.	A machine tap designed to curl the chip out ahead of the tap is called a __________ tap.

a.	Plug tap. 			b.  Helical fluted tap.

c.	Forming tap. 		d.  Gun tap.

8.	A machine tap designed to curl the chip out the top of the   hole instead of ahead of the tap is called a __________ tap.

a.	Plug tap. 			b.  Helical fluted tap.

c.	Forming tap. 		d.  Gun tap.

9.	Ground thread taps with oversize pitch diameter are designated by a letter:

a.	"E" for Extra large. 		b.  "B" for Bigger than normal.

c.	"H" for High limit. 		d.  "O" for Oversize.

10.	Tap drill sizes can be calculated by using the equation:

a.	Tap Drill Size = Outside Diameter -  (0.97 * Pitch).

b.	Tap Drill Size = Pitch Diameter + (0.97 * Pitch).

c.	Tap Drill Size = Major Diameter * Minor Diameter.

d.	Tap Drill Size = Major Diameter * (pitch  Lead) * 0.97.