Directions:  Circle or completely mark through the letter of the one most correct alternative.

1.	Hardness is:

a)	The opposite of plasticity.   		b)  Resistance to penetration.

c)	The same as brittleness.  		d)  The ability to absorb energy.

2.	Which property causes a metal to permanently retain its deformed shape after the deforming force has been removed?

a)	Plasticity. 				b)  Elasticity.

c)	Stress.  				d)  Strain.

3.	With respect to the 4-digit AISI system for classifying carbon and alloy steels, the first digit in the designation indicates the:

a)	Carbon content in weight percent.

b)	Carbon content in hundredths of a percent.

c)	Alloy subgroup or percent of the predominating alloy.

d)	Basic alloy type.

4.	Brass is an alloy composed of copper and:

a)	Aluminum. 				b)  Iron.

c)	Tin. 					d)  Zinc.

5.	With respect to the 4-digit AISI system for classifying carbon and alloy steels, the third, forth, and fifth digits in the designation indicates the:

a)	Carbon content in weight percent.

b)	Carbon content in hundredths of a percent.

c)	Alloy family.

d)	Alloy subgroup or percent of the predominating alloy.

6.	The ability of a metal to become permanently deformed by compressive forces is called:

a)	Elasticity.				b)  Plasticity.

c)	Malleability. 			d)  Ductility.

7.	The property of certain tool steels to retain hardness at high heat is called:

a)	Hardenability. 			b)  Refractory index.

c)	Red hardness. 			d)  Carbide formation.

8.	Which of the following is a common brand name for a cast alloy cutting tool material?

a)	Carboloy. 				b)  Stellite.

c)	Inconel. 				d)  Ferrite.

9.	The binder usually used to hold the grains of cemented carbide cutting tools together is:

a)	Cobalt. 				b)  Tungsten.

c)	Molybdenum.			d)  Vanadium.

10.	Carbon-tool-steel cutting tools start to lose their hardness in the temperature range

a)	200°F -300°F 				b)  300°F -400°F

c)	400°F -500°F 				d)  500°F -600°F