QUIZ # 12 • Section 16: Numerical Control

Directions:  Circle or completely mark through the letter of the one most correct alternative.

1.	There are two principal kinds of N/C systems: point-to-point and ___________.

a)	Line-to-circle.

b)	Contouring.

c)	Cartesian coordinate.

d)	DNC.

2.	The two dimensioning (more correctly, positioning) systems used for N/C machines are:

a)	Incremental/absolute.

b)	Direct/indirect.

c)	Tab sequential/word address.

d)	Floating/fixed.

3.	The two program formats used for most N/C machines are:

a)	Incremental/absolute

b)	Direct/indirect

c)	Tab sequential/word address

d)	Floating/fixed

4.	In N/C manual programming, preparatory functions (such as setting the controller to operate in metric units) are accomplished by the use of codes with the address word:

a)	G

b)	H

c)	I

d)	J

e)	M

f)	N

5.	The first computer-assisted N/C programming language was:

a)	APT

b)	AD-APT

c)	FORTRAN

d)	COBOL

e)	COMPACT II

f)	AUTOSPOT

End of Quiz