LAB 2

## Zero Crossing Detector

# Introduction

A zero crossing detector, Figure 1,  is a comparator op-amp circuit that goes into saturation when the sine wave input becomes greater then 0 Volts.  The output of

### FIGURE 1:  PSpice schematic.

the zero crossing detector op-amp goes into a passive differentiator circuit consisting of a capacitor and resistor.  The diode eliminates the negative part of the differentiated signal.  Since a pulse is needed for the positive and negative slopes of the 60 cycle sine wave, a mirror zero crossing detector is constructed that gives a positive pulse when the sine wave input becomes negative, Figure 2.

# FIGURE:  2

# P-SPICE Chart

Procedure:

- Build a zero crossing detector in P-Spice (ORCAD).  When constructing of the zero crossing detector the following parts will be needed: 15V power supply, 60Hz input signal, 2-A 741 op amp chips, 2-0.01(f capacitors, 2-D1N4002 diodes, 2-22k resistors, and a 1k resistor.

- After checking the operation of the circuit, construct the circuit.

- Check the operation of the circuit and include the output oscilloscope waveform, Figure 3, in your report.

- Write a report using the format style included in the web site.

### FIGURE:  3